## Slide 1
HSRP
Arctic Policy Document

## Slide 2
Only vessels that intend to operate within the Arctic and Antarctic areas as defined in the Polar Code need to comply with the code. The areas are as follows; Arctic: In general north of 60° N but limited by a line from Greenland; south at 58° - north of Iceland, southern shore of Jan Mayen - Bjørnøya – Cap Kanin Nos.

## Slide 5: Extreme Weather, Environmental Safety and Limited Infrastructure

## Slide 10
Even relatively simple monitoring of ships can reduce the potential for disaster. Ed Page, a former Coast Guard captain, runs a private-public partnership, the Marine Exchange of Alaska, that uses a network of radio receivers to watch over ships around Alaska. Exchange operators can contact vessels that are getting too close to shore — a ship should usually be far from land, so that in the event of a mechanical problem, it has time for repairs without running aground — and have them change course.
Captain Page acknowledged that if something went disastrously wrong with a ship within the 1.5 million square miles of ocean his network covers, “it would be ugly.”
“But we should stop worrying about what we’re going to do when things go wrong,” he said. “We should prevent things from going wrong.”
At the Marine Exchange of Alaska in Juneau, Shelby Martin monitors ship traffic through the state’s waters. Credit Michael Penn for The New York Times

## Slide 13
Vessel Monitoring and Tracking

## Slide 14
Bering Strait 2017
Bering Strait 2010

## Slide 16
299 meters, 96k DWT
113 meters, 5k DWT
111 meters, 3k DWT

## Slide 17
FLAGS OF VESSELS
13 Panamian
45 USA
39 Russian

## Slide 18
68 Cargo Vessels
24 Towing
15 Tankers

## Slide 20
Beaufort Sea Maritime Activity 2017
90 Vessels
41 Towing Vessels
35 Cargo Vessels
8 Fishing Vessels
6 Passenger Vessels
3 Tankers
5 Sailing
2 Military

## Slide 21: Maritime Domain Awareness & Maritime Domain Management
Addressing marine safety and environmental protection issues with benefit of good information.
Exxon Valdez Oil Spill
Overseas Ohio

## Slide 22
“… take appropriate action to expand the AIS tracking network …”
“Completion of an AIS receiver network in the Arctic is high priority; linkages between AIS and marine mammal awareness need to be developed.”

## Slide 23
Polar Code

## Slide 26
Dynamic Marine Protected Areas and Navigational Hazards
IMO Polar Code

## Slide 28
Polar Waters Operations Manual

## Slide 29
Ice Classed Vessels

## Slide 30: Polar Code Ship Categories
Category A
Notes: Top Row: Aiviq (Ice Class A3), Timofey Guzhenko (Ice Class Arc6)
Middle Row: Nanuq (Ice Class A0), Nathaniel B. Palmer (Ice Class A2)
Bottom Row: Miss Marilene Tide (Ice Class PC7), Costa Deliziosa (no ice class)

## Slide 31
Category B
Polar Code Ship Categories
Notes: Top Row: Aiviq (Ice Class A3), Timofey Guzhenko (Ice Class Arc6)
Middle Row: Nanuq (Ice Class A0), Nathaniel B. Palmer (Ice Class A2)
Bottom Row: Miss Marilene Tide (Ice Class PC7), Costa Deliziosa (no ice class)

## Slide 32
Category C
Polar Code Ship Categories
Notes: Top Row: Aiviq (Ice Class A3), Timofey Guzhenko (Ice Class Arc6)
Middle Row: Nanuq (Ice Class A0), Nathaniel B. Palmer (Ice Class A2)
Bottom Row: Miss Marilene Tide (Ice Class PC7), Costa Deliziosa (no ice class)

## Slide 33
USCG-MXAK CRADA (Cooperative Research and Development Agreement)
AIS transmission tests conducted with Coast Guard cutter Healy
“Arctic Next Generation Navigational Safety Information System”

## Slide 34
Arctic Next Generation Navigational Safety Information System
Builds upon AOOS AIS/WX project to communicate information to vessels via AIS;
Virtual aids to Navigation (i.e. buoys)
Locations of whalers
Environmental Data (i.e. weather and ice)
Locations of whales
Vessels in distress, etc.
Notify vessels in “Areas to be Avoided” or exceeding speed restrictions

## Slide 35
AIS Atons in Alaska

## Slide 36
Virtual Buoys – AIS ATONS

## Slide 38
Arctic Maritime Safety Net Project

## Slide 41
(187) Mariners should be aware that Alaskan Natives engage in subsistence whaling in the Beaufort Sea near Point Barrow in the spring from March through June and in the fall from September through November. Vessel operators are requested to contact the Alaska Eskimo Whaling Commission at 907-852-2392 or 800-478-2392 or aewcdir@barrow.com prior to entering this area for information about the location and avoidance of traditional Native hunting parties.
(116) Point Hope 22 miles NW of Cape Thompson and 102 miles from Cape Krusenstern, is the seaward extremity of a low tongue of land that projects 16 miles W from the general line of the coastal mountains. Subsistence whaling at Point Hope occurs in the spring (April-May) and fall (September-October) as far as 30 miles offshore. Vessels transiting in the vicinity of Point Hope during these times are requested to contact the Alaska Eskimo Whaling Commission and the Point Hope communications center on VHF-FM channel 68.
Subsistence harvesting of Beluga whales occurs at Point Lay during the months of June and July and vessels should contact the Point Lay telecommunications center on VHF-FM channel 68 if transiting in the area during this time.

## Slide 49
Vessel Monitoring and Tracking

## Slide 50
Tanker Transits 2017
Tanker Transits 2018

## Slide 51
M/V Selendang Ayu
No Information
No Maritime Domain Awareness and No Maritime Domain Management
Loss of Life, Loss of Property, Major Oil Spill

## Slide 52: INFORMATION - NO TIME Maritime Domain Awareness No Offshore Routing Measures No Maritime Domain Management

## Slide 55
Providing Information and Validating Compliance

## Slide 56
From January 1, 2018 to December 31, 2018 there were 2,482 cargo vessel transits within 100 miles of shore made by 777 individual vessels.
1,543 of these transits were made less than 25 miles offshore.
  62.17% of transits made outside Monterey Bay, CA in 2018 were less than 25 miles offshore, a majority were 16-21 miles off shore.

## Slide 57
Weather Stations – Data Transmitted via AIS

## Slide 58
Cruise ships Transiting Whale Waters Automatic generation of e-mail and text msg alerts

## Slide 59
NOME Environmental Data – Buoy
Current and Waves

## Slide 61
Reduced Speed: 1600, Jan 23, 2019
Not Under Command: 0550, Jan 24, 2019
Taken Under Tow by Denise Foss: 0710, Jan 28, 2019

## Slide 62: Vessel Adherence to Routing Measures

## Slide 63
130 AIS Receivers
28 AIS Transmitters 49 WX Stations

## Slide 65: Risk Mitigation Offshore Routing and Use of Safe Passes

## Slide 71
HSRP Arctic Paper
Information to Mariners
Dynamic Coast Pilot
Ice and Weather Information
Updated Charts
Voyage Planning – Polar Operations Manual
Information to Agencies – USCG
Validation of Adherence with Polar Code
Emergency Response – Environmental Conditions