## Slide 1: Benefits and Opportunities from NOAA’s Coastal Zone Products
Brian K. Batten, Ph.D., CFM

## Slide 2: NOAA does so much for the coastal community!

## Slide 3: Agenda
SLR Scenarios – supporting community use
Water Level Gages – improving accessibility and align products
Rainfall – the other flood hazard for coastal communities

## Slide 4: Community Use of SLR Rise Scenarios

## Slide 5: From the established past to an uncertain future

## Slide 6: Outcomes of uncertainty
Ralph Stacey Complexity Matrix

## Slide 7: Federal Scenarios for the NCA
2012 Guidance
Risk tolerance guidance
2017 Update

## Slide 8: Scenario Approaches
Approach | Benefits | Drawbacks
Pick a curve - Choose curve, use values at time slices for planning | Simple | Justification for buy-in to specific curve
Representative Values – Single values per time horizon balancing curves | Simple Balances uncertainty | Limited look at vulnerability progression Misses extremes
Multiple Scenarios – Sample curves at each time | Discreet representation of full range Full representation of uncertainty | Can complicate follow-on application Many values, additional guidance needed to use
Incremental Values – Equal increment increases, assess vulnerability | Detailed look at vulnerability progression, back into timing of adaptation actions | Extensive analysis, interpretation

## Slide 9: “Empirical” data…

## Slide 10: The other flood hazard for coastal communities…

## Slide 11: Virginia Beach – 2016 Heavy Rainfall – Opened Eyes
Is the recent increase in heavy rainfall frequency short-term statistical noise or part of a long-term historical trend?
What kind of future trend (if any) is being projected by long-range Global Climate Models?
Does the City need to take steps now by increasing its design rainfall guidance?
July 31 - heavy rainfall
  500 to 1000-yr recurrence interval at the 2-hr duration
September 19 – Julia
  100 to 200-yr event at the 24-, 48-hr durations
October 8-9 – Matthew
  500 to 1000-yr event at the 24-hr durations

## Slide 12: Historical Rainfall Analysis
Gage (Norfolk
Local (Hampton Roads)
Regional (Mid-Atlantic Seaboard)
Moderate/high confidence that frequency & intensity is increasing

## Slide 13: Future Rainfall Projections
Medium and High emission scenarios RCP 4.5 and 8.5
Bias correction
Variable resolution (11 & 44 km)
Peaks over Threshold
Probability Frequency Curves

## Slide 14: Increasing Rainfall Findings and Actions
Atlas 14 guidance may be underestimating the local design rainfall by 7-10%
Future projections support increases of 5% for the intermediate scenario to 24-27% in the high scenario by 2060
Historical trends suggest a 20% increase in standard given a 40-year design horizon

## Slide 15: Water Level Observation Data

## Slide 16: Water Level Data to Assess Inundation
Post-disaster damage assessments
Informs recovery resource allocation
  Primary Use:
  Storm Surge Model Validation

## Slide 17: Accessing Water Level Data

## Slide 19: Challenges
Currently need 4+ custom methods that access the federal agency APIs or gage tables to collect metadata and data.
  USGS, NOAA, NWS (aggregator), USACE, State/Local
Different standards for
  Horizontal and vertical datum
  Date & time
  Reporting intervals and historical time periods

## Slide 20: Gage Sourcing Complicates the Process
FOR EACH Agency:
  Acquire and plot gage positions
  Investigate duplicates (cross/intra-agency gages)
  Find metadata (gage datum)
  Query data
  Convert elevations to NAVD88, if possible
  Remove gages with no data and no datum
Merge

## Slide 21: Recommendations
Sea Level Rise
Quantify and publish acceleration
Improve guidance to help communities
Rainfall
Non-stationarity analysis
Update Atlas 14, and in context of non-stationarity
Water Level Data
Enable download of multiple station records
One federal data standard and access portal